## Slide 1
3 Phase Bridge Rectifier– 36MT160
  VRRM = 1600V IF(AV) = 35A VF(max) = 1.19V RѲJC = 1.35 °C / W
  At maximum we draw 2kW power at 180V level. At this level maximum load current is 11.1 A.
  Ploss(max) = 11.1 * 1.19 = 13.2W
  Temperature increase 1.35 * 13.2 = 17.8 °C at maximum condition.

## Slide 2
Freewheeling Diode – MUR1560G
  VRRM = 600V IF(AV) = 15A VF(max) = 1.50V RѲJC = 4.25 °C / W
  Ploss(max) = 11.1 * 1.5 = 16.65W
  Temperature increase 4.25 * 16.65 = 70.7 °C at maximum condition.
  Max efficieny is not targeted, diode is ultra-fast rectifier then switching losses will be ignored.

## Slide 3
IGBT– IXGH24N60C4D1
  VRRM = 600V IC = 30A VCE(sat) = 1.90V RѲJC = 0.8 °C / W Eon = 1.0 mJ Eoff = 1.1 mJ
  Ploss(con) = 11.1 * 1.9 = 21.1 W
  We use 1 kHz switching frequency;
  Ploss(sw) = 1kHz * (1+1.1)mJ = 2.1 W
  Temperature increase 0.8 * (2.1+21.1) = 18.6 °C at maximum condition.